## Slide 1: Introduction to 3d printing
By: David Garvin

## Slide 2: Agenda
Types of 3d printers
Types of materials used in 3D printing
Websites to find items to print
Overview of 3D printing software options
Popular printer manufacturers and models
Examples of 3D printing

## Slide 3: FDM Printing (Fused Deposition Modeling)
  Extrudes filament through nozzle to build objects layer by layer
  Most common type
  Filament-based
  Easiest to use
<Insert a picture or drawing of your prototype here>

## Slide 4: Resin Printing (SLA)
  Uses light to solidify liquid resin to build object layer by layer
  Best for high detail
  Difficult to clean/cure
  Difficult to use

## Slide 5: Other types of 3d printing
  Gel printing
  Laser powder bed fusion (LPBF)
  Concrete 3d printing

## Slide 6: Types of 3d printing materials
  PLA – biodegradable, cheap, easy to print
  PETG – water resistant, strong, flexible, challenging to print
  ABS – heat resistant, UV resistant, difficult to print
  TPU – flexible, very difficult to print
  Infused (Metal/Wood/Glass Fiber/Carbon Fiber) – added strength, ability to apply stain (wood), needs high temp capable printer
  Resin – best for high detail, fragile, significant post process work

## Slide 7: Where to find prints
  MakerWorld.com
  Thingiverse.com
  Printables.com
  Thangs.com
  Cults3D.com
  MyMiniFactory.com

## Slide 8: 3D printing software
  Design
  Tinkercad – beginner friendly
  Fusion 360 – powerful CAD
  Blender – for organic shapes
  FreeCAD – open source
  Shapr3D – designed for iPad
  Prepare
  Bambu Studio
  Cura
  Prusa
  Orca

## Slide 9: Current Printer Market
  Bambu Lab (199 to 2,899) – fast, beginner friendly
  Prusa (429 – 9,990) – reliable, enthusiast favorite
  Creality (169 – 1,299) – budget friendly
  Anycubic/Phrozen (Resin & FDM) (349 – 849) – budget friendly for resin
  Elegoo (Resin & FDM) – (169 – 2,499) – fast and reliable resin

## Slide 10: What to look for when selecting a printer
  Decide what you will be using it for
  Where will you keep the printer
  Build volume size
  Max nozzle temp
  Nozzle size/resolution
  Auto bed leveling (Must)

## Slide 11: Questions and printed examples